## Slide 1: NetApp FAS6210 Shared Low Tier Standard Architecture
Mike Arndt, Systems Engineer
2011-09-06

## Slide 2: Overview
New Shared Low Tier Standard Architecture:
  FAS6210 HA Pair
  DS4243 shelves of 2TB 7.2k SATA drives
    4 shelves in base configuration
    6 shelves in maximum configuration (with 8.1)
  512GB of FlashCache per controller
  10GbE connectivity for data access
  1GbE connectivity for management
  Software licenses:
    NFS, CIFS, and iSCSI protocols
    SnapMirror, SnapVault, and SnapRestore
    Multistore and Deduplication

## Slide 3: Requirements and Limitations
The FAS62xx platform requires ONTAP 8.0.1 or higher
  Standard ONTAP version will initially be 8.0.1P5
ONTAP 8.0.x does not support Online DataMotion for vFilers
  Offline DataMotion for vFilers still supported
ONTAP 8.1 will support DataMotion for vFilers
  Due to be GA by the end of CY2011
ONTAP 8.1 required for larger aggregates
  70TB max aggr size with 8.0, 162TB max aggr size with 8.1
  Adding 2 shelves to the 4 shelf base configuration requires 8.1 in order to still use 1 aggregate per controller
65 vFilers per controller continues to be the limit
5 meter limit as maximum distance from controllers to all disk shelves

## Slide 4: Capacity and Performance Scaling
Base config of 4 shelves per cluster:
  112TB usable
Maximum config of 6 shelves per cluster
  170TB usable
Peak throughput at 32k 50/50 read/write mix:
  637MB/sec per controller
    20,400 IOPs per controller
Peak IOPs at 4k 50/50 read/write mix:
  42,750 IOPs per controller
    166MB/sec per controller
Performance profile limits:
    7.5MB/sec per TB
    503 IOPs per TB
    These values assume possible performance degradation during a cluster failover event

## Slide 5: FAS/V6200 Controller I/O Standalone Controller
10GbE
e0a, e0b
Management
ACP
USB
(disabled)
e0M / SP
GbE
e0c, e0d, e0e, e0f
Vertical I/O
Slot 1
PCIe v2.0
Slots
Slots 3,4,5,6
8Gb FC
0a, 0b, 0c, 0d
Serial
Console
10/100 Ethernet
NVRAM8
(Slot 2)

## Slide 6: Controller Configuration Details

## Slide 7: SAS Connectivity Details
Cable shelf to shelf IOMs from OUT ● to IN ■
A stack shelf IDs start with 00 and count up
B stack shelf IDs start with 10 and count up

## Slide 8: ACP Connectivity Details
Cable shelf to shelf ACPs from OUT ● to IN ■
Use locked wrench port on FAS6210 for ACP connections

## Slide 9: Network Connectivity Details
The SP (new version of the RLM) is the wrench port on the FAS6210
The locked wrench port on the FAS6210 is used for ACP connectivity to the shelves
The e0a 1GbE port is used for management network connectivity
  This should be a 1GbE connection, not 100Mb
The e0c and e0e 10GbE ports should be used to create a LACP “ifgrp” for data access
  An ifgrp is the 8.x equivalent of a vif in 7.x
The e0d and e0f 10GbE ports are used to create a 2nd LACP ifgrp as required

## Slide 10: Initial Cabinet Layout

## Slide 11: Final Cabinet Layout

## Slide 12: Aggregate Sizing and Growth
ONTAP VERSION | ONTAP 8.0.1P5 or higher
AGGREGATE CONFIGURATION | 1 64bit aggregate per controller Aggregate snap reserve set to 0 and aggregate snapshots disabled Note: vol0 will reside on the data aggregate
RAID GROUP SIZE | 15 drives per raid group Note: aggregates should be grown in 9 or 15 drive increments
INITIAL CONFIGURATION 2 DS4243 shelves per controller 4 DS4243 shelves total | 1 aggregate of 3 raid groups (45 drives) per controller 3 spare drives per controller 56TB usable per controller = 112TB total
ONTAP VERSION | ONTAP 8.1 or higher
MAX SIZE WITH GROWTH 3 DS4243 shelves per controller 6 DS4243 shelves total | 1 aggregate of 4.5 raid groups (69 drives) per controller 3 spare drives per controller 85TB usable per controller = 170TB total

## Slide 13: Dedication Solution Considerations
Some dedicated storage systems may have a similar configuration as the Shared Low Tier
Deviations from the Shared Low Tier platform that are acceptable include:
  Installation in a single cabinet based on a known capacity growth maximum
  Fewer protocols licensed, as most dedicated storage controllers do not require CIFS and iSCSI